- First remove the four bolts holding the front half of the front fender, remove front half of front fender (Figure 1).

- Remove the push rivet in the center holding the plastic chrome fork guard, remove the two 5mm allen head bolts on the front side of the cover, remove plastic chrome fork guard.

- Remove the two end cap bolts from either side of the Traxxion Fork Brace.

- Loosen the four alignment bolts (do not remove them).

- Look at the back of your new Traxxion Fork Brace (Figure 2) you will notice two machined indentions in the brace.  The longer horizontal indention goes on the right side (if you are on the bike) facing the rear of the motorcycle.  The shorter vertical indention goes on the left side (if you are on the motorcycle facing towards the rear of the bike)

- Slip the brace into place (Figure 2).  Seat the brace down as low as possible making sure the brace is level across both forks (Figure 3).

- Re-install the two end caps.

- Snug up the end cap bolts (do not tighten yet).  Close the gap in the front first then tighten the rear bolt.

- Make sure the brace is level then fully tighten the end cap bolts to 12lb/ft.

- Once the end cap bolts are tight then tighten the top (4) alignment bolts to 6lb/ft.

- Reinstall the front half of the front fender.

| Figure 1 | Figure 2 | Figure 3 |
| --- | --- | --- |

Once installed the fork brace should look like the picture below.

See reverse side for Fork Guard Installation Instructions.

- Remove both end cap bolts from your Traxxion Fork Brace.

- Slip the Fork Guard into place making sure the notch on the lower portion of the guard is facing in towards the wheel.

- Once in place re-install the two end cap bolts on either side.  Tighten the front bolt first to reduce the gap between the two halves, then tighten the rear bolt.  Do not over tighten.  You should tighten the end cap bolts to more then 12lb/ft.

When completed yours should look something like the picture below.